## Slide 1: Two Tank Interacting System
CH303: Process Control
Ankit Gond
Sayed Musaraf Ali
Dept. of Chemical Engineering, IIT Ropar.

## Slide 2: Process diagram
State variables/ controlled variable: h2
Manipulated variables: q1
Disturbance variable: qi
Objective:
To study dynamics, stability, and control of the liquid levels in the system.

## Slide 3: Process parameters
Parameter name | Value
Cross-sectional area of tank 1 (A1) | 3 ft2
Cross-sectional area of tank 2 (A2) | 5 ft2
Flow coefficient between the two tanks (C1) | 8 cfm/ft1/2
Flow coefficient for the outlet of tank 2 (C2) | 12 cfm/ft1/2

## Slide 4: Empirical Modelling of Nonlinear Chemical Processes

## Slide 5: Steady-State Identification and Initial Conditions
Set the time derivatives
Now Steady State equations :
Now using these values in flow rate equations to find steady state h1 and h2

## Slide 6: Development of empirical models: First Order/ FOPTD Models
Chemical Unit/Plant
Input Signal (u)
Output response(y)
Steps involved in developing the predictive model:
Data collection: Perturb the process through an input step signal, and record the output process data.
Model Selection: Through analysis of nature of output data, assume a suitable model form (first order transfer function or first order plus time delay model), between input and output variable (controlled variable), disturbance and controlled variable.
System Identification: Estimating the unknown parameters of the chosen model (i.e., process gain, time constant) through regression modelling approaches.
Cross Validation: Once the parameters are identified, validate the developed model with the collected data.

## Slide 10
Regression method
Consider estimating parameters of FOPTD model i.e.,
M = Step change in input variable = 10% or 20% of Inlet Flow rate = 1.6 or 3.2
Unknown parameters here :
Define error function, =
Objective function:
subject to:
Method of identifying transfer function parameters

## Slide 11: Parameters and Errors (Approx.)
Parameters | 10 % Input | 20 % Input | Mean
Kp (Process Gain) | 0.24 | 0.25 | 0.24
Tau | 4.00 | 4.12 | 4.06
Time Delay | 0 | 0 | 0
Mean Squared Error (MSE) is used as a metric to evaluate the performance of the model. (70% Training Datasets and 30% Validation Datasets)
Validation MSE for 10% step change | 0.0004
Validation MSE for 20% step change | 0.0004

## Slide 13: Stability Analysis & Feedback Control Design

## Slide 14: Procedure for Closed Loop Stability Analysis
System Setup:
Use the parameters Kp, τ, and time delay obtained from the designed FOPTD model.
Implement the two-tank system as a closed-loop system with proportional (P) control.
Stability Analysis:
Define the closed-loop transfer function using the FOPTD model and the P controller gain Kc​.
Analyze the characteristic equation for stability using the Routh-Hurwitz criterion or root locus method.
Evaluate the system's poles to determine stability, focusing on whether all poles lie in the left half-plane (for continuous-time systems).
Characteristic equation;
Validation:
Simulate the closed-loop response for a range of Kc​ values to observe stability behavior and oscillations.
Identify the critical gain (Kc_critical) where the system transitions from stable to unstable.

## Slide 15: Feedback Control Design
P Controller Design:
The P controller [ was implemented to adjust the inflow rate based on the error between the setpoint and the tank level
The gain Kc​ was selected based on the stability analysis results to ensure a balance between fast response and stability.

## Slide 18: Conclusions
Conclusion of Project Task 1:
Modeled the two-tank system using FOPTD approximation, identifying key parameters Kp​, τ, and θ.
Achieved accurate system response for 10% and 20% step changes with low MSE, validating the model.
Analyzed steady-state conditions and added noise to simulate real-world behavior.
Conclusion of Project Task 2:
Stability analysis showed a stable system with a single pole at -0.248.
Designed a P controller using parameters from Project Task 1 for effective setpoint tracking and disturbance rejection.
Ensured system stability with minimal overshoot and steady-state error through proper tuning.

## Slide 19: Key Learnings from the Course and Project-Based Learning:
Dynamic System Modeling: Gained hands-on experience in modeling real-world processes using FOPTD approximation.
Stability and Control: Learned to analyze system stability using tools like root locus and designed effective feedback control.
Optimization and Parameter Estimation: Developed skills in tuning parameters for accurate system behavior and performance.
Noise Handling: Understood the impact of noise in real systems and methods to mitigate its effects in control applications.
Practical Application: Bridged theory and practice by applying control principles to a simulated two-tank system, enhancing problem-solving and critical thinking.

## Slide 20
THANK YOU